## Slide 1
ECE 5159-Class 4
DIGITAL SYSTEM DESIGN WITH VHDL
Engr. Professor Alice Oluwafunke Oke
Department of Computer Engineering, ACU, Oyo

## Slide 2
Information is represented in VHDL code as data object.
Types of Data Objects
Signals
Constants
Variables.
Signals are the most important data objects for describing logic circuits
constants and Variables are sometimes useful but infrequently used.
VHDL DATA OBJECTS

## Slide 3
The rules for specifying data object names are:
Any alphanumeric character as well as the “_” underscore character, i.e.
Alphabets A to Z (VHDL is not case sensitive) and
Digits 0 to 9
DATA OBJECTS NAMES
Caveats of Data Objects
It cannot be a VHDL keyword
It must begin with a letter
It cannot end with underscore
It cannot have two successive underscores.

## Slide 4
DATA OBJECTS NAMES
Examples of Valid Data Objects Names
Mohd4, Zara, Xyz, move_name,
a_123, j, Byte x-y
Examples of Invalid Data Objects Names
1x, _zara, a__123, move_name_

## Slide 5
VHDL KEYWORDS
Keywords are reserve words by VHDL because they have special meaning to the programme
Examples of Keywords are:
ENTITY ARCHITECTURE SIGNAL BIT
TYPE VARIABLE CONSTANT FOR PORT COMPONENT PACKAGE CASE USE PROCESS WHILE OF
ELSE GENERIC DOWNTO IF

## Slide 6
Signal can mean either a
VHDL data object or
Logic signal in a circuit
To avoid confusion the VHDL data object is written as SIGNAL
SIGNAL data object is used to represent
Individual logic signals in a circuit. i.e. ‘0’ or ‘1’
Multiple logic signals i.e. “1001”
Binary numbers (integers). Either “1001” or 9
DATA OBJECTS VALUES AND NUMBERS

## Slide 7
SIGNAL data objects represent the logic signals or wire in a circuit.
Three places where signals are declared in VHDL code:
an entity declaration
Declarative section of architecture
Declarative section of a package
SIGNAL DATA OBJECTS

## Slide 8
SIGNAL declaration
Signal is always declared with an associated type as follows:
SIGNAL signal_name : type_name
The signal’s type_name determines the legal values that the signal can have and its legal uses in VHDL code
SIGNAL DATA OBJECTS Contd

## Slide 9
Kinds of Signal types
BIT
BIT_VECTOR
STD_LOGIC
STD_LOGIC_VECTOR
STD_ULOGIC
SIGNED
UNSIGNED
INTEGER
ENUMERATION
BOOLEAN
SIGNAL DATA OBJECTS Contd

## Slide 10
BIT and BIT_VECTOR
Objects of BIT type can have the values ‘0’ or ‘1’.
An object of BIT_VECTOR type is a linear array of BIT
objects.
SIGNAL Y1 : BIT ;
SIGNAL j : BIT_VECTOR (I TO 4) ;
SIGNAL Byte : BIT_VECTOR (7 DOWNTO 0) ;
SIGNAL DATA OBJECTS Contd

## Slide 11
The multibit signal j represents four BIT objects. It can
be used as a single four-bit quantity, or each bit can be
referred to individually.
The syntax for referring to the signals individually is j(I),
j(2), j(3). and j(4). An assignment statement such as
j <= "1010";
results in j( 1 )=1 , j(2)=0, j(3)=I, and j(4)=0.
BIT and BIT_VECTOR Contd

## Slide 12
The signal Byte comprise eight BIT object . The assignment statement
Byte <= "10011000";
results in Byte( 7 )=1, Byte(6)=0, and so on to Byte(0)=0.
BIT and BIT_VECTOR Contd

## Slide 13
VHDL packages serves as a repository, it is used to hold VHDL code that is of general use, like the code that defines a type, which can then be used in other source code files.
A package can have 2 parts:
package declaration
package body (this is an optional part)
VHDL PACKAGE

## Slide 14
The general form of a package declaration is
PACKAGE package_name IS
[TYPE declarations]
[SIGNAL declarations]
[COMPONENT declarations]
END package_name ;
in order to use the definitions provided in the PACKAGE,
such as the definition of a TYPE, two statements must
be included
LIBRARY library_name ;
USE library_name.package_name.all ;
VHDL PACKAGE Contd

## Slide 15
The library_name represents the location in the computer file system where the package is stored.
A Library can either be:
System library when it is provided as part of a CAD system. An example of a system library is the ieee library
User library when it is created by the user. An example:
LIBRARY work :
USE work.user_package_name .all ;
VHDL PACKAGE Contd

## Slide 16
Packages in ieee library are
std_logic_1164
std_logic_signed
std_logic_unsigned and
std_logic_arith
VHDL PACKAGE Contd

## Slide 17
The STD_LOGIC type was added to the VHDL Standard in IEEE 1164.
It provides more flexibility than the BIT type. To use this type, two statements must be included
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
These statements provide access to the std_logic_1164 package, which defines the STD_LOGIC type.
STD_LOGIC AND STD_LOGIC_VECTOR

## Slide 18
Legal values for a STD_LOGIC data object:
0, 1, Z, -, L, H, U, X and W.
Only the first four are useful for synthesis of logic circuits.
STD_LOGIC AND STD_LOGIC_VECTOR Contd

## Slide 19
STD_LOGIC AND STD_LOGIC_VECTOR Contd
STD_LOGIC Data Object | REPRESENTATION
Z | high impedance
- | don't care
L | Weak 0
H | Weak 1
U | Uninitialized
X | Unknown
W | Weak unknown

## Slide 20
The STD_LOGIC_VECTOR type represents an array of
STD_LOGIC objects.
SIGNAL xl, x2, Cin, Cout, : STD_LOGIC;
SIGNAL C : STD_LOGIC_VECTOR (I TO 4);
SIGNAL X, Y, S : STD_LOGIC_VECTOR (3 DOWNTO 0):
STD_LOGIC objects are often used in logic expressions in VHDL code. STD_LOGIC_VECTOR signals can be used as binary numbers in arithmetic circuits by including in the code the statement
USE ieee.std_logic_signed.all;
STD_LOGIC AND STD_LOGIC_VECTOR Contd

## Slide 21
STD_LOGIC type is a subtype of the STD_ULOGIC type.
The only difference between STD_ULOGIC and STD_LOGIC is the concept of a resolution function.
A resolution function is used to determine what value a signal should take if there are two sources for that signal.
STD_ULOGIC TYPE

## Slide 22
For example:
Two In-state buffers could both have their outputs connected to a signal, Y.
At some given time one buffer might produce the output value ‘Z’ and the other buffer might produce the value ‘1’.
A resolution function is used to determine that the value of Y should be 1 in this case.
The STD_LOGIC type allows multiple sources for a signal; it resolves the connect value using a resolution function that is provided as part of the std_logic_1164 package. The STD_ULOGIC type does not permit signals lo have multiple sources
STD_ULOGIC TYPE Contd

## Slide 23
For example:
Consider two buffers Z and 1 as shown
STD_ULOGIC TYPE Contd
Z
1
Y
Z
1
Y = Z
Y = 1
Resolution Function

## Slide 24
The SIGNED and UNSIGNED Signal types are defined as std_logic_signed and std_logic_unsigned type in the package called std_logic_arith.
The package defines circuit that are used to implement arithmetic operators such as +, *.
SIGNED and UNSIGNED types are identical to the STD_LOGIC_VECTOR type because they represent an array of STD_LOGIC signals.
SIGNED AND UNSIGNED TYPE

## Slide 25
The SIGNED type is used in code for circuits that deal with signed (2’s complement) numbers i.e. negative numbers
while
The UNSIGNED type is used in code that deals with unsigned numbers i.e. positive numbers
SIGNED AND UNSIGNED TYPE Contd

## Slide 26
Example:
Assume that A and B are signals with the SIGNED type. Let A has the value “1000" and B = “0001".
For the comparison
A < B = True
because A = -8 and B = 1
While
if A and B are signals with the UNSIGNED type,
then For the comparison
A < B = False
because A = 8 and B = 1.
SIGNED AND UNSIGNED TYPE Contd

## Slide 27
An INTEGER signal represents a binary number.
The code does not specifically give the number of bits in the signal, as it does for STD_LOGIC_VECTOR signals.
By default, an INTEGER signal has 32 bits and can
represent numbers from -(231 - 1) to 231 - 1.
SIGNAL X : INTEGER RANGE: - 127 TO 127 ;
This defines X as an eight-bit signed number.
INTEGER TYPE

## Slide 28
An object of type BOOLEAN have the values TRUE or
FALSE, where
TRUE is 1 and
FALSE is 0.
SIGNAL Flag : Boolean ;
BOOLEAN TYPE

## Slide 29
A SIGNAL of ENUMERATION type is one for which the possible values that the signals can have are user specified. The general form is
TYPE enumerated_type_name IS (name {, name1}) ;
The most common example of using the ENUMERATION type is for specifying the states for a finite-state machine
TYPE State_type IS (stateA, stateS, stateC) ;
SIGNAL y : State_type ;
ENUMERATION TYPE

## Slide 30
A CONSTANT is a data object whose value cannot changed.
Unlike a SIGNAl, a CONSTANT does not represent a wire in a circuit.
The general form of a CONSTANT declaration is
CONSTANT constant_name : type_name := constant_value;
The purpose of a constant is to improve the readability of code, by using the name of the constant in place of a value or number.
CONSTANT DATA OBJECT

## Slide 31
Example:
CONSTANT Zero : STD_LOGIC_ VECTOR (3 DOWNTO 0) := "0000" ;
Then the word Zero can be used in the code to indicate the constant value "0000".
CONSTANT DATA OBJECT Contd

## Slide 32
A VARIABLE unlike a SIGNAL, does not necessarily represent a wire in a circuit.
VARI­ABLE data objects are sometimes used to hold the results of computations and for the index variables in loops
VARIABLE DATA OBJECT

## Slide 33
VHDL provides Boolean, Arithmetic and relational operators.
They are categorized according to the precedence of the operators as shown.
OPERATORS
 | OPERATOR CLASS | OPERATOR
Highest Precedence | Miscellaneous | **, ABS, NOT
 | Multiplying | *, /, MOD, REM
 | Sign | +, -
 | Adding | +, -, &
 | Relational | =, /=, <, <=, >, >=
Lowest Precedence | Logical | AND, OR, NAND, NOR, XOR, XNOR

## Slide 34
This Logic expression
x1 AND x2 AND x3 OR x4
does not have the meaning of
x1 * x2 * x3 + x4
because AND does not have precedence over OR.
It is also not a legal VHDL expression.
To be both legal and have the desired meaning, it must be written as
(x1 AND x2 AND x3) OR x4
OPERATORS Contd

## Slide 35
VHDL DESIGN ENTITY
A circuit or subcircuit described with VHDL code is called a design entity, or just entity.
An entity has two main parts:
The entity declaration
The architecture
General structure of an entity

## Slide 36
VHDL DESIGN ENTITY Contd
ARCH ITECTURE architecture_name OF entity_name IS
[SIGNAL declarations]
[CONSTANT declarations]
[TYPE declarations]
[COMPONENT declarations]
[ATTRIBUTE specifications]
BEGIN
{COMPONENT instantiation statement ;}
{CONCURRENT ASSIGNMENT statement ;}
{PROCESS statement ;}
{GENERATE statement ;}
END [architecture_ name] ;