## Slide 1
ECE 5159-Class 5
DIGITAL SYSTEM DESIGN WITH VHDL
Engr. Professor Alice Oluwafunke Oke
Department of Computer Engineering, ACU, Oyo

## Slide 2
A VHDL entity defined in one source code file can be used as a subcircuit in another source code file.
In VHDL, subcircuit is called a component
A subcircuit must be declared using a component declaration
COMPONENT fulladd
PORT (Cin, x, y : IN STD_LOGIC;
s, Cout : OUT STD_LOGIC);
END COMPONENT ;
USING SUBCIRCUITS

## Slide 3
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
PACKAGE fulladd_package IS
COMPONENT fulladd
PORT (Cin, x, y : IN STD_LOGIC;
s, Cout : OUT STD_LOGIC); END COMPONENT ;
END fulladd_package ;
DECLARING A COMPONENT IN A PACKAGE

## Slide 4
A Concurrent assignment statement is used to assign a value to a signal in an architecture body. E.g.
s <= x XOR y XOR Cin
VHDL provides four different types of concurrent assignment statements
CONCURRENT ASSIGNMENT STATEMENTS
Simple signal assignment
Selected signal assignment
Conditional signal assignment
Generate statements

## Slide 5
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY fulladd IS
PORT (Cin, x, y : IN STD_LOGIC;
s, Cout : OUT STD_LOGIC); END fulladd ;
ARCHITECTURE Logicfunc OF fulladd IS
BEGIN
s <= x XOR y XOR Cin ;
Cout <= (x AND y) OR (x AND Cin) OR (y AND Cin);
END Logicfunc ;
CODE FOR A FULL ADDER

## Slide 6
Simple Signal assignment
EXAMPLE OF CONCURRENT ASSIGNMENT STATEMENTS
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY fulladd IS
PORT (Cin, x, y : IN STD_LOGIC;
s, Cout : OUT STD_LOGIC);
END fulladd ;
ARCHITECTURE Logicfunc OF fulladd IS
BEGIN
s <= x XOR y XOR Cin;
Cout <= (x AND y) OR (x AND Cin) OR (y AND Cin);
END Logicfunc ;

## Slide 7
Selected Signal assignment
Selected signal assignment allows a signal to be assigned one of several values based on a selection criterion.
Consider a multiplexer: a combinational circuit that selects one of n input lines and provides it on the output with the block diagram and Truth Table as shown
EXAMPLE OF CONCURRENT ASSIGNMENT STATEMENTS

## Slide 8
The Selected Signal assignment for the multiplexer is as shown:
EXAMPLE OF CONCURRENT ASSIGNMENT STATEMENTS
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY mux2to1 IS
PORT (d0, d1, s : IN STD_LOGIC;
Z : OUT STD_LOGIC);
END mux2to1 ;
ARCHITECTURE Behaviour OF mux2to1 IS
BEGIN
WITH s SELECT
Z <= d0 WHEN ‘0’;
d1 WHEN OTHERS;
END Behaviour ;

## Slide 9
Conditional Signal assignment
Conditional signal assignment is similar to selected signal assignment. It allows a signal to be set to one of several values. An example using the mux2to1 is
EXAMPLE OF CONCURRENT ASSIGNMENT STATEMENTS
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY mux2to1 IS
PORT (d0, d1, s : IN STD_LOGIC;
Z : OUT STD_LOGIC);
END mux2to1 ;
ARCHITECTURE Behaviour OF mux2to1 IS
BEGIN
Z <= d0 WHEN s = ‘0’ ELSE d1 ;
END Behaviour ;

## Slide 10
Generate Statement
Generate statement is often used to describe regularly structured hierarchical code.
An example of such circuit is a 16-to-1 multiplexer using five instances of a 4-to-1 multiplexer subcircuit or a 4-bit ripple-carry adder using four instances of full adder.
This structure of a regular code for a 16-to-1 multiplexer can be written in a more compact form using a loop.
VHDL provides a feature called the FOR GENERATE statement for describing such regularly structured hierarchical code.
EXAMPLE OF CONCURRENT ASSIGNMENT STATEMENTS

## Slide 11
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY fulladd IS
PORT (Cin, x, y : IN STD_LOGIC;
s, Cout : OUT STD_LOGIC); END fulladd ;
ARCHITECTURE Logicfunc OF fulladd IS
BEGIN
s <= x XOR y XOR Cin ;
Cout <= (x AND y) OR (x AND Cin) OR (y AND Cin);
END Logicfunc ;
EXAMPLE OF N-RIPPLY ADDER CIRCUIT AND CODE
Consider this 3-input full adder

## Slide 12
The circuit for the 3-input full adder
CI+1 = X1Y1 + C1X1 + Y1C1
= X1Y1 + CI (X1 + Y1)
= g1 + p1c1
Where g1 = X1Y1, and p1 = (X1 + Y1)
The Analysis
EXAMPLE OF N-BIT RIPPLE CARRY ADDER CIRCUIT
AND CODE

## Slide 13
The symbol of an n-bit ripple-carry full adder is presented
EXAMPLE OF N-BIT RIPPLE CARRY ADDER CIRCUIT

## Slide 14
A 4-bit ripple-carry full adder
EXAMPLE OF N-BIT RIPPLE CARRY ADDER CIRCUIT

## Slide 15
The VHDL code for a 4-bit ripple-carry full adder
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY adder4 IS
PORT (Cin : IN STD_LOGIC;
x3, x2, x1, x0 : IN STD_LOGIC;
y3, y2, y1, y0 : IN STD_LOGIC;
s3, s2, s1, s0 : IN STD_LOGIC;
Cout : OUT STD_LOGIC);
END adder4 ;
ARCHITECTURE Structure OF adder4 IS
SIGNAL c1, c2, c3 : STD_LOGIC;
COMPONENT fulladd
PORT (Cin x, y : IN STD_LOGIC;
s, Cout : OUT STD_LOGIC);
END COMPONENT;
BEGIN
stage0: fulladd PORT MAP (Cin, x0, y0, s0, c1);
EXAMPLE OF N-BIT RIPPLE CARRY ADDER CODE

## Slide 16
stage1: fulladd PORT MAP (Cin, x1, y1, s1, c2);
stage2: fulladd PORT MAP (Cin, x2, y2, s2, c3);
stage3: fulladd PORT MAP (
Cin => c3, Cout => Cout, x => x3, y => y3, s => s3);
END Structure ;
EXAMPLE OF N-BIT RIPPLE CARRY ADDER CODE Contd

## Slide 17
Another type of assignment statement provided by VHDL is sequential assignment statements, the order of the statements in the code are executed sequentially. The order is significant in Sequential but not in Concurrent assignment statements.
The semantics of the code can be affected if done otherwise
The three variants of the sequential assignment statements are:
SEQUENTIAL ASSIGNMENT STATEMENTS
IF statement
CASE statement
Loop statement

## Slide 18
The PROCESS statement is used to separate sequential statements from concurrent statements.
The PROCESS statement appears inside an architecture body and it encloses other statements within it.
The IF, CASE, and LOOP statements can appear only inside a PROCESS.
The general form of these statements are:
PROCESS STATEMENT

## Slide 19
[process_label;]
PROCESS [(signal name {, signal name} )]
[VARIABLE declarations]
BEGIN
[WAIT statement]
[Simple Signal Assignment Statements]
[Variable Assignment Statements]
[IF Statements]
[CASE Statements]
[LOOP Statements]
END PROCESS [process_label] ;
General Form of a PROCESS STATEMENT

## Slide 20
IF expression THEN
statement ;
{statement ;}
ELSIF
statement ;
{statement ;}
ELSE
statement ;
{statement ;}
ENDIF;
General Form of an IF STATEMENT
E.g.
IF Sel = ‘0’ THEN
F <= x1 ;
ELSE
F <= x2 ;
ENDIF;
SEL | X1 | X2 | F=MUL
0 | 0 | 0 | 0
0 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 21
EXAMPLE OF PROCESS STATEMENT USING IF-THEN-ELSE
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY mux2to1 IS
PORT (d0, d1, s : IN STD_LOGIC;
Z : OUT STD_LOGIC);
END mux2to1 ;
ARCHITECTURE Behaviour OF mux2to1 IS
BEGIN
PROCESS (d0, d1, s )
BEGIN
IF s = ‘0’ THEN
Z <= d0 ;
ELSE
Z <= d1 ;
END IF ;
END PROCESS ;
END Behaviour ;
PROCESS STATEMENT using if-then-else statement for 2-to-1 Multiplexer

## Slide 22
ALTERNATIVE CODE FOR IF-THEN-ELSE STATEMENT
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY mux2to1 IS
PORT (d0, d1, s : IN STD_LOGIC;
Z : OUT STD_LOGIC);
END mux2to1 ;
ARCHITECTURE Behaviour OF mux2to1 IS
BEGIN
PROCESS (d0, d1, s )
BEGIN
Z <= d0 ;
IF s = ‘1’ THEN
Z <= d1 ;
END IF ;
END PROCESS ;
END Behaviour ;

## Slide 23
CASE STATEMENT
A case statement is similar to selected signal assignment in that the case statement has a selection signal and includes WHEN clauses for various valuations of this selection signal
PROCESS STATEMENT WITH CASE STATEMENT
The general form of a CASE statement and the CASE STATEMENT for 2-to-1 Multiplexer are presented next

## Slide 24
CASE expression IS
WHEN constant_value =>
statement ;
{statement ;}
WHEN constant_value =>
statement ;
{statement ;}
WHEN OTHERS =>
statement ;
{statement ;}
END CASE ;
General Form of a CASE STATEMENT

## Slide 25
EXAMPLE OF PROCESS STATEMENT USING CASE STATEMENT
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY mux2to1 IS
PORT (d0, d1, s : IN STD_LOGIC;
Z : OUT STD_LOGIC);
END mux2to1 ;
ARCHITECTURE Behaviour OF mux2to1 IS
BEGIN
PROCESS (d0, d1, s )
BEGIN
CASE s IS
WHEN ‘0’ =>
Z <= d0 ;
WHEN OTHERS =>
Z <= d1 ;
END CASE ;
END PROCESS ;
END Behaviour ;

## Slide 26
VHDL code that describes a process statement of a 2-to-4 binary decoder using a CASE statement

## Slide 27
[loop_label;]
FOR variable_name IN range LOOP
statement ;
{statement ;}
END LOOP [loop_label] ;
General Form of LOOP STATEMENTS
[loop_label;]
WHILE boolean_expression LOOP
statement ;
{statement ;}
END LOOP [loop_label] ;

## Slide 28
Write a VHDL code to represent the months of the year using a CASE statement
ASSIGNMENT